How to commission
safe (FSoE) ctrlX DRIVE 
under EtherCAT control
Version 01

Content

1. General information	3

2. FSoE Settings	5

2.1. EtherCAT (TwinCat3) drive implementation	5

2.2. Task settings	6

2.3. Safety Settings of TwinCAT	7

2.4. Safety Settings of ctrlX DRIVE	10

2.5. Test of State Machine	11

# 1. General information

In the following we show to you how you commission a Fail Safe over EtherCAT (FSoE) ctrlX DRIVE under an EtherCAT (in here TwinCAT 3) control.

Topology

Fig. : Topology

Versions used

All the functions and screen shots are based on:

- ctrlX DRIVE Engineering version >= 01V14

- ctrlX DRIVE firmware/runtime version >= AXS-T-0305

- TwinCAT 3

Prerequisites

The Beckhoff TwinCAT system and ctrlX DRIVE Engineering have been successfully installed on your PC and started.

Used hardware

The ctrlX DRIVE and EtherCAT components used for this document are:

Fig. : ctrlX DRIVE components used

Fig. : Beckhoff EtherCAT components used

In particular the following units were used:

- Beckhoff EtherCAT coupler EK1914

- Beckhoff EtherCAT communication interface EL6900

- 2x Beckhoff EtherCAT 4-channel digital inputs

# 2. FSoE Settings

## 2.1. EtherCAT (TwinCat3) drive implementation

Start NC default project and add EtherCAT Master!

Fig. : Add EtherCAT master

Add your drives via Scan or manually!

Fig. : Add connected drives via Scan

Set Engineering over EtherCAT (EoE) settings and activate configuration!

Fig. : Set EoE settings

After activation the “Master” should be in RUN mode and drives should be found via EoE connection.

Fig. : ctrlX DRIVE connected found over EoE connection

## 2.2. Task settings

Fig. : Task settings

Add two Variables for Error acknowledging (ErrAck) and for distinguishing “Run” and “Stop” condition (Run_Stop)!

Fig. : Add variables ErrAck and Run_Stop

## 2.3. Safety Settings of TwinCAT

Add new SAFETY item!

Fig. : Add new safety item

Select used devices in the project (can also be deleted later). Otherwise a compile error occurs.

Fig. : Select used devices

Set the FSoE addresses (same as drive settings)!

Fig. : Set FSoE addresses

Set the FSoE adresses of the used so called “Terms”!

Fig. : Set FSoE adresses of used Terms

Add function block e.g. safe decouple to Network.

ErrAck and Run_Stop get linked automatically.

Fig. : Add safe function block to Network

Create your inputs and assign them!

Fig. : Assign inputs

Link Run_Stop/ErrAck to Variables!

Fig. : Link variables ErrAck and Run_Stop

Choose your target system and adjust the Safe Address!

Fig. : Choose target system and adjust safe address

Password must be entered again.

Fig. : Login via Password

If Verification works without error Download the project!

Fig. : Verify and download safety project

After project download LED Diag 4 blinks -> Force ErrAck, LED Diag 4 should now light up permanently.

Force output Run_Stop as well!

Fig. : Force Run_Stop and ErrAck

## 2.4. Safety Settings of ctrlX DRIVE

Fig. : Set Safety bus communication and FSoE slave address

Fig. : Configure profile

## 2.5. Test of State Machine

Fig. : Test normal Operation Mode

Fig. : Test Safe Emergency Stop (SMES)

Fig. : Test Safe Operational Stop (SMST2)

Fig. : Test Safe Motion (SMM1)